## Slide 2: Integrated River Engineering Project / Catalogue of Measures Danube East of Vienna
16. September 2016

## Slide 3: Danube East of Vienna
Approx. 48 km long From: Freudenau Power Plant (River-km 1.921,0)
To: Austrian-Slowak border (River-km 1.872,7)
© via donau I 3
Notes: funded within the TEN-T program

## Slide 4
Deficits Danube East of Vienna (1)
Riverbed degradation
Heavily regulated river in National Park area
Inadequate fairway depths
 decoupling of river and floodplains, falling groundwater levels
 habitats of typical local flora and fauna are at risk
 limited competitive-ness of inland water-way transport

## Slide 5
Deficits Danube East of Vienna (2)
Deficit: Objective:
Riverbed degradation …  Riverbed stabilisation
Heavily regulated river …  Renaturation
Inadequate fairway depths …  Improving fairway conditions
Framework conditions:  maintaining the free-flowing character of the stretch  no negative impact on flood protection
High diversification of objectives
 need for interdisciplinary cooperation / planning
 need for wider stakeholder participation

## Slide 6: Pilot projects east of Vienna
2002 - LIFE
Side Arm Reconnection
Orth
2014 - TEN-T
River Bed Stabilization, River Bank Restoration, Side Arm Reconnection, Groyne Optimisation
Bad Deutsch-Altenburg
2004 - LIFE
Side Arm Reconnection
Schönau
2009 - TEN-T
River Bank Restoration
Groyne Optimisation
Witzelsdorf
1998
Side Arm Reconnection
Haslau-Regelsbrunn
2006 - LIFE
River Bank Restoration
Thurnhaufen

## Slide 7: Pilot Project Bad Deutsch-Altenburg
Project Area
approx. 3 km long stretch (stream-km 1887.5 – 1884.5)
Aims
testing the Granulometric River Bed Improvement to counteract river bed degradation
realizing all measures foreseen for the Danube east of Vienna in one stretch for the first time
gaining experience and reducing technical and economical risks for future projects

## Slide 8: Pilot Project Bad Deutsch-Altenburg
B
B
B
A
C
C
C
D
B
Project Area: approx. 3 km long stretch (stream-km 1887.5 – 1884.5)
Bad Deutsch-Altenburg
Hainburg
Reconnection of the Johler Side Arm, 1,4 km long. Discharge of 10 m³/s at low water
D
River Bank Restoration - removal of 1,2 km stone amour along the river bank
C
Optimization of Groynes – new location and new shapes -19 old +10 new groynes
B
Granulometric River Bed Improvement. Approx. 120.000 m³ of coarse gravel
A

## Slide 9: Some Results
Granulometric riverbed stabilisation is technically feasible within strict quality requirements. It is now „state of the art“.
Overrun tests confirmed compatibility with navigation (propulsion).
Contribution of coarser gravel to riverbed stability was over-estimated by numerical and physical models.
Groynes have a significant influence on the river bed.
New habitats establish after short periods of higher water levels and were populated nearly immediately.
© via donau I 9

## Slide 10: Results Monitoring of bedload transport
l: 8 – 11 m
D: 0.25 – 0.30 m
Animation: Team Abiotisches Monitoring (BOKU)
Dunes with height of max. 45 cm
After dredging, dunes migrate by approx. 5,6 m/h in the dredging field
Significant influence on riverbed stability & discussion of fairway depths
Time of measurement
Speed: 2.5 – 9.0 m/h
Average: 5.6 m/h

## Slide 11: Pilot Project Sediment Management
Shallow section Orth
(1902,7 -1901,1)
Dredging sites
(1888,4 – 1886,1)
Dumping sites
(1906,8-1906,2; 1904,6-1903,4)
Monitoring area ~18 km
Some of the topics of the pilot project:
Impact on river bed
Economic aspects of sediment management (prices, quantity per day, equipment in use)
Sustainability of dredging & dumping activities
Duration 10.03 - 05.05.2015 relocation of 68.500 m³ of gravel
2 dredging sites
2 dumbing sites
2 contractors

## Slide 12
Pilot Project Witzelsdorf Optimisation
Construction of new groynes
Removal of old groynes and river bank restoration
By-pass route for young fish and for reducing sedimentation in the groyne field
4 new downstream-facing groynes lead to higher dynamics along the river bank
innovative groyne shapes – advantages for ecology and navigation
by interdisciplinary planning
removal of the 8 existing groynes
1,2 km river bank restoration
Lowering of the training wall to 0,5 m over LNWL
Unwanted gravel deposition
Training wall +0,5 m
+0,65 m
+0,65 m
+0,4 m
+0,4 m
Original construction period: 2007-2009
2015: Optimisation by the adaption of the new groynes
Improvement of ecological conditions

## Slide 13: The way forward …
Current analysis show
… that the pilot projects, together with the fairway maintenance have significantly reduced river bed degradation between 2010 and 2015
… that most of the fairway maintenance work is concentrated on a handful spots
Solid foundation for future works
Practical experiences from implementing 6 pilot projects
Practical experiences of „small-scale sediment management“ within fairway maintenance since 2008 (excavated gravel is transported upstream)
Results of a pilot project on sediment management realised in 2015
New developments in waterway management (WAMS) and traffic management (DoRIS Services)
As planned, the results of the pilot phase have been incorporated in the implementation of the measures for the Danube east of Vienna.

## Slide 14
Continuation of the integrative approach within the framework of the Integrative River Engineering Project
Combining the outcome of the pilot projects with the new developments in waterway and traffic management
… within the “Catalogue of Measures for the Danube east of Vienna”
The overall objectives remain the same:
 Stabilising water levels
 Improving fairway conditions and optimising waterway infrastructure
 Improving the ecological conditions of the wetlands within the Donau-Auen National Park
Integrated River Engineering Project / Catalogue of Measures

## Slide 15
New implementation strategy Turning away from a large scale project towards processes and small optimisation projects:
To stabilise water levels, processes have benefits over single projects (integrative sediment management)
To improve the habitat quality of the wetlands and the navigation conditions, small optimisation projects are realised in parallel.
Realisation in order by priority.
Priority 1: Realisation by 2022 (Action Programme Danube of the MoT) Priority 2: Realisation by 2030
Integrated River Engineering Project / Catalogue of Measures

## Slide 16
Processes / Integrative Sediment Management
opportunity for continuous improvement over the years.
possibility to react on the effects of the work of previous years, on discharge, etc.
Types of processes
Relocation of gravel (upstream)
    gravel excavated in the course of maintenance dredging
    gravel excavated in bedload traps
Local addition of coarser gravel
Integrated River Engineering Project / Catalogue of Measures

## Slide 17
Optimisation projects
Step by step realisation in order by priority
Types of optimisation projects
Optimisation of low water regulation
    “More regulation” in critical fords
    “Less regulation” in sections with river bed degradation
Side arm reconnection
River bank restoration
Stabilisation of critical scours
Smaller measures like the adaption of piers, traffic management projects, etc.
Integrated River Engineering Project / Catalogue of Measures

## Slide 18
In total: 642.106 m³ within 3 years 214.035 m³ per year
ü
6
One big bottleneck? - dredging east of Vienna 2013-2015

## Slide 19
Supporting processes
Scientific supervision / Monitoring to measure the impact of the measures and to ensure ongoing “Learning from the river” also in future.
Continuation of stakeholder participation to integrate stakeholders from ecology and navigation and civil society.
    Possibility to accompany and influence the implementation of the Catalogue of Measures.
    Discussion on guiding principles for future management of the free-flowing section.
Integrated River Engineering Project / Catalogue of Measures

## Slide 20
Thank you for your attention!
Robert TÖGEL
Head of Team Integrated River Engineering Project
T +43 50 4321-2612 robert.toegel@viadonau.org Donau-City-Straße 1, 1220 Vienna
www.viadonau.org/FGP
The Integrated River Engineering Project and the Pilot Projects Bad-Deutsch Altenburg and Witzelsdorf were co-financed by the European Union within the Trans-European Transport Network (TEN-T) Programme

## Slide 21: Minimal available fairway depths 2015 (2014)
Wachau East of Vienna
224 days >= 25 dm
(222 days 2014)
323 days >= 25 dm
(352 days 2014)
Framework conditions: gauge Wildungsmauer 2015 on 55 days under low water level < 162cm
Fairway conditions

## Slide 22
What the customers say …