## Slide 1: Upper Danube River Basin, Germany Flood Protection and Revitalization works
Klaus Arzet

## Slide 2: Agenda
Flood protection issues along the Danube River -General findings after the flood event June 2013
Major elements of flood protection measures
„Option A +“ : Smooth development, enhancing hydromorphological active structures

## Slide 4
Deggendorf June 2013 – damage 1,3 billion €
Notes: HW-Ereignisse sind Naturereignisse.
früher schon immer gegeben - auch in Zukunft mit Extremereignissen rechnen
Hochwassergedächtnis (vor allem, wenn man nicht direkt Betroffener war) vergisst leider nur allzu schnell.
Bild der HW-Katastrophe bei Neustadt während des Pfingst-HWs 1999 - rd. 23 Mio. m³ in den Polder ergossen - rd. 700 Gebäude betroffen, rd. 70 Mio. € Schadenssumme
Thema: Überregionale HW-Schutzplanung Donau im Wesentlichen Ergebnisse einer Untersuchung vorstellen, die die TUM (Strobl, Rutschmann) derzeit an der Donau durchführt
Betrachtung von größeren Retentionsräumen an der Donau und ihre Wirkungen auf extreme Hochwasserabflüsse
Ergebnisse für den oberen Abschnitt zwischen Neu-Ulm und Kelheim liegen bereits vor. Der östliche Abschnitt und eine Gesamtbetrachtung der Dnau ist derzeit in Bearbeitung.

## Slide 5: dike failure at Auterwörth
Straubing
Deggendorf
Vilshofen
Bogen
Plattling
flooded area app. 9 km2
app. 19 mio. m3
Niederalteich

## Slide 6: June 4, 2013, 10:30 Uhr: dike failure near Auterwörth after overflow
Quelle: Eckl, FFW Winzer

## Slide 7: Dike failure Isar
Straubing
Deggendorf
Vilshofen
Bogen
Plattling
flooded area app. 22 km2
app. 51 mio. m3
Fischerdorf

## Slide 8
Notes: Fischerdorf

## Slide 9
Effect of flood polder -
dike failures 4th June 2013
simulation
measured

## Slide 10: Immediate measures in 2013 - 2015
Immediate reconstruction of destroyed or heavily damaged dikes
Rehabilitation of flooded or damaged pumping stations
Reestablishment of the former degree of protection by
  - protection against animals like beavers
  - improvement of stability
  - addition of missing dike ways
Approvement of 59 km dikes with technical gaskets
like steel pillings or slurry walls (interior sealing)
Expenses 2013: 17 Mio. €, 2014: 30 Mio. €; 2015: 11 Mio. €
Notes: Schlitzwand: slurry wall
Spundwand: steel pillings

## Slide 11: Major Objective: Protection against a 100-year flood along the Danube River between Straubing and Vilshofen

## Slide 12: (Developement of Danube waterway) + flood protection against a 100-year flood + Smooth Developement of River Danube between Straubing and Vilshofen founding bodies: Federal Republic of Germany and Federal State of Bavaria
Major Objective of current project

## Slide 13: Flood plain of HW100 (Stand: ROV)
Straubing
Deggendorf
Vilshofen
Bogen
Plattling
Targets for flood protection
Protection against
100-year flood for existing
settlements
industrial areas
important structural facilities

## Slide 14: Targets for flood protection
Protection against a 100-year flood for existing
settlements
industrial areas
important structural facilities
Notes: Punkt 1: Landesentwicklungsprogramm Bayern
Punkt 2 (Erhöhte Wasserstände durch Bewuchs Hochwasser 2002 (50 cm) und flussbauliche Regelung (10 cm))
Punkte 3 bis 5 WHG (Wasserhaushaltsgesetz Bund)
14

## Slide 15
Elements for flood protection (I)
second dike
line
Notes: Second dike line
For Agricultural used areas the present degree of protection is adequate
So protection for a 100 yaer flood is only necessary for settlements

## Slide 16: Example for a second dike line – Polder Steinkirchen

## Slide 17: Bavarian flood polder programm
HQ frequent
HQ extreme
Effect of flood protection measures
Natural
Retention
technical
flood protection
flood polder
remaining
risk

## Slide 18: Elements for flood protection (II)
Relocation
of dike
Notes: Relocation of dikes nearer to the settlemens

## Slide 19: Elements for flood protection (III)
heightening
of existing dikes
Notes: Hightening of existing dikes

## Slide 20: Already realised flood protection measures
Expenses so far: ~ 200 Mio. €
Finalisation planned until 2024
Total investment costs : 660 Mio. €

## Slide 21: Realisation of the project
Realisation until 2024
Total investment costs : 660 Mio. €

## Slide 22
Danube river and tributaries as
major corridors for fish migration

## Slide 23
Potamodrome Species: short migration distances (rivers)
Diadrome Species: long migration distances (sea/rivers)
Classification of measures relevant for fish migration
along technical weirs in federal shipping ways
source: bfg/LfU
Notes: Donau, Landesgrenze BW bis Kelheim |  |  | 
Umsetzung von Maßnahmen zur Verbesserung der Durchgängigkeit |  |  | 
Stand: 8.9.2015 |  |  | 
Nr. | Staustufe (lech bis Vohburg) | Ansprechpartner | Stand (bisher umgesetzt, derzeit in Planung, vorgesehen bis 2021 bzw 2027
1 | Vohburg | WWA IN | Durchgängig
2 | IN | WWA IN | Durchgängig, Einweihung war im Juli 2015 (techn. FAA (Schlitzpass), durch EON gebaut)
3 | Bergheim | WWA IN | Durchgängig seit 2010 (im Zuge DAD-Projekt)
4 | Bittenbrunn (oberhalb Neuburg) | WWA IN | nicht Durchgängig, derzeit in Planung, Umsetzung i.R. des Projektes Polder Riedenheim
5 | Bertholdsheim | WWA IN | nicht Durchgängig, derzeit in Planung (durch EON)
6 | Donauwörth | WWA DON, BEW | nicht Durchgängig, derzeit in Planung (durch BEW, Umgehungsgerinne) bis 2021
7 | Schwenningen | WWA DON, BEW | nicht Durchgängig, laut aktuellem Entwurf des MNP bis 2021
8 | Höchstädt | WWA DON, BEW | nicht Durchgängig, laut aktuellem Entwurf des MNP bis 2027
9 | Dillingen | WWA DON, BEW | nicht Durchgängig, laut aktuellem Entwurf des MNP bis 2027
10 | Faimingen | WWA DON, BEW | nicht Durchgängig, laut aktuellem Entwurf des MNP bis 2027
11 | Gundelfingen | WWA DON, BEW | nicht Durchgängig, laut aktuellem Entwurf des MNP bis 2027
12 | Offingen | WWA DON, BEW | nicht Durchgängig, laut aktuellem Entwurf des MNP bis 2021
13 | Günzburg | WWA DON, BEW | nicht Durchgängig, laut aktuellem Entwurf des MNP bis 2021
14 | Leipheim | WWA DON, BEW | nicht Durchgängig, laut aktuellem Entwurf des MNP bis 2021
15 | Elchingen | WWA DON, BEW | nicht Durchgängig, laut aktuellem Entwurf des MNP bis 2021
16 | Böfingerhalde | WWA DON, BEW | Durchgängig, Umgehungsgerinne

## Slide 24
Implementation of concepts for improvement
of hydromorphological status along federal shipways
FWK ohne UK
FWK mit UK
Danube consruction works/
flood protection
„Option A +“
Notes: Hinsichtlich der Zuständigkeit für die Umsetzung der im Maßnahmenprogramm bzw. den Bewirtschaftungsplänen festgelegten Maßnahmen zur Erreichung der Ziele der Wasserrahmenrichtlinie (WRRL) bestehen Divergenzen zwischen dem Freistaat Bayern und dem Bund.
Die Verpflichtung zur wasserwirtschaftlichen Gewässerunterhaltung – welche unter Beachtung der Ziele der WRRL zu erfolgen hat und den Anforderungen entsprechen muss, die im Maßnahmenprogramm an die Gewässerunterhaltung gestellt sind (§ 39 Abs. 2 Wasserhaushaltsgesetz (WHG)) – obliegt unstreitig dem Bund. Bezüglich der wasserwirtschaftlichen Ausbaupflicht hingegen bestehen unterschiedliche Rechtsauffassungen. Nach bayerischer Auslegung ist der Bund als Eigentümer der Bundeswasserstraße Donau (Art. 39 Abs. 1 Nr. 1 i. V. m. Art. 22 Abs. 1 Nr. 1 a. E. Bayerisches Wassergesetz, § 4 Abs. 1 WHG) und nicht der Freistaat in der Verantwortung. Der Bund erkennt dies jedoch bisher nicht an.
Im Rechtsausschuss der Länderarbeitsgemeinschaft Wasser (LAWA-AR) in dem die Angelegenheit behandelt wurde, wird die bayerische Position von den anderen Ländern mehrheitlich geteilt.
Eine Einigung ist bislang noch nicht abzusehen.

## Slide 25
„Option A +“ : Danube ecological river construction works
„Option A+“:
Make use of hydromorphological measures to optimize ecological status in the Danube
Integrative concept „vision of all possibilities“, implemented on the long run with regard to revitalization, natural development and NATURA 2000 concepts, flood plain restoration and ecological maintenances of riverbed
But: Timeline of projects which improve river navigation and flood protection along the river should not be delayed
Model stretches help to develop a common understanding and design for ecological components like i.e. removal of river embankments or connecting meanders
Main objective of Bavarian Government is to develope a common solution with the Federal Government which combines the hydraulic construction work without an additional weir = so called Option A +

## Slide 26
flattened banks,
gravel areas
for fish breeding
deadwood,
breakwaters,
pools
removal of river embankment,
connecting old meanders
new riverbed branch
Deadwood,
Breakwaters,
pools
removal of river
embankment
revitalized banks,
gravel islands
removal of embankment,
connecting old meanders
removal of river embankment,
new river branch
river continuity
at inflow of river Altmühl
dredging and
connecting old meander
revitalized riverbed branch
new riverbed branch
riffles
Hydromorpological measures

## Slide 27
Hydromorphological measures and NATURA 2000
Effects of hydromorphological measures on NATURA 2000 areas
Dialogue between water management and nature conservation authorities in order to coordinate measures (major objectives: avoid conflicts in an early state, make use of synergies)

## Slide 28: Public Relations
Numerous information events
New exhibition at Schiffmeisterhaus, Deggendorf
Information pavilions
Roadshow
Mobile PC terminals
Films
. . . details see www.lebensader-donau.de

## Slide 29: Thank you for your attention